## Slide 1: Principles of Theater Practices
Module 6 – Light applications

## Slide 2: Its not a light bulb – it’s a lamp!
Lamp = the lighting element that emits the light
Fixture = the functional or decorative item that holds the lamp as well as provides the power. The fixture may also contain a switch
  Another name for a fixture is a Luminaire

## Slide 3: A practical light or fixture
A scenic element that functions to some degree as a light source

## Slide 4: Conventional vs LED

## Slide 5: Conventional fixtures
Par cans
Fresnel
Ellipsoidal reflector spotlight (ERS)

## Slide 6: Par cans
Simplest design
Came in 3 sizes
  Par 38, 56, 64
One focus adjustment
  Vertical or horizontal oval
Beam width adjustments required swapping out lamps
Can be colored using gel
Gets HOT!

## Slide 7: Fresnel
Unique lens design
One focus adjustment
  Adjustable size circle of light
Can be colored using gel
Gets HOT!

## Slide 8: Ellipsoidal reflector spotlight (ERS)
Many adjustments
  Focus
  Shutter
  Hotspot
  Barrel rotation
Size of beam can be changed by swapping lenses
Can be colored using gel
Can have a pattern (GOBO) installed
Gets HOT!

## Slide 9: Shape of reflector and adjustable lenses is how you can get pattern

## Slide 10: Gel and GOBOS
Gel is colored media
  Originally was made form gelatin
  Now made of plastic or glass
Also called a color filter
GOBO = Go Between
  Also called pattern or a template
Can be made of steel or glass

## Slide 11: Accessories
Barn doors
Top hat/half hat
Gel frame
Iris
GOBO rotator
GOBO scroller

## Slide 12: Cyc lights
Either individual cells or bands of 3-4
High light output
Gets VERY hot

## Slide 13: Strip lights
Many circuits so chase effects can happen
Smaller form factor
Good for up lighting
Good for lighting backdrops/cycs
Can be colored using gel
Gets HOT!

## Slide 14: Foot lights
Fixtures downstage that provide a front/up light
Does help illuminate under hats and over head props (umbrellas)
Used for a vaudeville aesthetic

## Slide 15: Follow spotlight
Used to track actors/performers around the stage
Requires an operator
Has the ability to adjust color/focus/iris

## Slide 16: Controlling conventional fixtures
Lightboard sends commands
Commands sent over cable to dimmer room
Each dimmer has an address
When address is called a percentage 0-100 is sent to dimmer
Electricity from dimmer sent to light fixture
Lamp in fixtures glows at the percentage requested

## Slide 17: Defining terms
Light board
  Console that lighting commands come from – programable
Address
  The unique number/location of a dimmer
Dimmer
  Conventional electrical device that can vary amounts of electricity
Circuit
  The network of wires, dimmer and plug unique to one address

## Slide 18: Moving fixtures (movers)
Can move on command without manual interaction
Often have build in color wheels (gel)
Often have a built-in set of GOBOs
  Also gobo rotation
Often have built-in focus
Have a built-in douser
  Possible mechanical strobe
Use a bright light source
  Last up to ~2000hrs
  Gets HOT!
Requires constant power source

## Slide 19: Controlling intelligent fixtures
Pan left to right 0 - 270 degrees
Tilt front to back -90 - +90 degrees
Intensity 0 -100
Shift focus in – out
First color wheel 1-16
Second color wheel 1-16
Gobo selection 1-16
Gobo rotation
Facet (splits gobo into 3)
Facet rotation
Douser open – closed
Each feature needs an individual control, because of this intelligent fixtures require more than one address, in fact, an address is needed for each feature in use.
Some moving light can use 56 address

## Slide 20: LED instruments
These are also called intelligent fixtures
The simplest of fixtures just turn on/off
  Most have other capabilities
Communicates using same light board (DMX)
Most have built in dimmers
Most require constant power source

## Slide 21: DMX (digital multiplex)
DMX is the communication protocol for modern lighting equipment
Uses a 3 or 5 pin connector or RJ45
  Fixtures are daisy chained
Light boards talk to dimer racks as well as intelligent lights with these commands
Fixtures are assigned a starting address using DIP switches or a menu
An address can be in the range of 1 – 512
Address # of multi-address lights cannot overlap

## Slide 22: LED par
Wide range of colors from one fixture
Lighter weight
Can strobe
Long life from LEDs
Only gets warm

## Slide 23: LED LIKO equivalent
Wide range of colors from one fixture
Can use same lenses as conventional fixtures
Light weight
Can strobe
Long life from LEDs
Only gets warm

## Slide 24: LED mover
Wide range of colors from one fixture
Lighter weight
Can strobe
Long life from LEDs
Only gets warm

## Slide 25: LED strip lights
Color changing
Some are foxed position
  Some can move
Can do effects
  Strobe
  Color chase